USER MANUAL

RS232 GPS RECEIVER

BR-304J

Company Name: GLOBALSAT TECHNOLOGY CORPORATION

2-1F, No. 16, Chien 8 Rd, Far East Century Park,

Chung Ho City, Taipei Hsien, Taiwan

Tel:886-2-82263799      Fax:886-2-82263899

Web: www.globalsat.com.tw

E-mail: service@globalsat.com.tw

Specification

Product Feature

- “SiRF Star Ⅱ/LP” high performance and low power consumption chipset

- All-in-view 12-channel parallel processing

- Built-in active antenna

- High sensitivity to satellite signal

- Cold start under 45 seconds, average

- Superior urban canyon performance

- FoliageLock for weak signal tracking

- Build-in SuperCap to reserve system data for rapid satellite acquisition.

- Supported NMEA 0183 command: GGA, GSA, GSV, RMC, GLL, VTG

- Super-cohesive magnetic for mounting on the car

- LED indicator for GPS fix or not fix

- Water resisted and non-slip on the bottom

- RS232 interface connection port

System Specification

| Electrical Characteristics (Receiver) |  |  |
| --- | --- | --- |
| Frequency |  | L1, 1575.42 MHz |
| C/A Code |  | 1.023 MHz chip rate |
| Channels |  | 12 |
| Sensitivity |  | -170 dBW |
| Accuracy |  |  |
| Position Horizontal |  | 15m 2D RMS (SA off) |
| Velocity |  | 0.1m/sec 95% (SA off), |
| Time |  | 1 micro-second synchronized to GPS time |
| WAAS enabled |  | 10m 2D RMS |
| Datum |  |  |
| Datum |  | WGS-84 |
| Acquisition Rate |  |  |
| Hot start |  | 8 sec., average (with ephemeris and almanac valid) |
| Warm start |  | 38 sec., average (with almanac but not ephemeris) |
| Cold start |  | 45 sec., average (neither almanac nor ephemeris) |
| Reacquisition |  | 0.1 sec. average (interruption recovery time) |
| Protocol |  |  |
| GPS Protocol |  | Default: NMEA 0183 (Secondary: SiRF binary) |
| GPS Output Data |  | SiRF binary >> position, velocity, altitude, status and control ; NMEA 0183 protocol, and supports command: GGA, GSA, GSV, RMC, VTG, GLL (VTG and GLL are optional) |
| GPS transfer rate |  | Software command setting (Default : 4800,n,8,1 for NMEA ) |
| Dynamic Condition |  |  |
| Acceleration Limit |  | Less than 4g |
| Altitude Limit |  | 18,000 meters (60,000 feet) max. |
| Velocity Limit |  | 515 meters/sec. (1,000 knots) max. |
| Jerk Limit |  | 20 m/sec**3 |
| Temperature |  |  |
| Operating |  | -30°~ 80°C |
| Storage |  | -40°~ 85°C |
| Humidity |  | Up to 95% non-condensing |
| Power |  |  |
| Voltage |  | 5V ±5% |
| Current |  | 90mA typical |
| Physical Characteristics |  |  |
| Dimension |  | 2.32" x 1.85" x 0.82" (59mm x 47mm x 21mm) |
| Cable Length |  | 1620 +- 10mm |
| Low Noise Amp |  |  |
| Amplifier Gain w/out cable |  | 27 dB Typical |
| Filtering |  | -25dB (+100 MHz) |
| Output VSWR |  | 2.0 Max. |
| Voltage |  | DC 3 ~ 5.0V |
| Current |  | 15mA max.@5VDC |

 RS232 GPS RECEIVER   

Due to continuous product improvements, all specifications may be subject to change without notice

LED indictor:

LED OFF:		Receiver switch off

LED ON:		No fixed, Signal searching

LED flashing:		Position Fixed

Pin Assignment & Diagram

| PIN | Signal |
| --- | --- |
| P1 | Ground |
| P2 | Command data from the iHFK to the GPS module |
| P3 | GPS NMEA data from the GPS module to the iHFK |
| P4 | Vcc (Power) 5.0  5% VDC |

# NMEA Output Command

1.The GGA-Global Positioning System Fix Data describes Time, position

and fix related data for a GPS receiver.

The format is as following:

$GPGGA,HHMMSS.sss,DDMM.mmmm,d,DDDMM.mmmm,d,q,ss,h.h,a.a,z,,,,*CC

<CR><LF>

$            			Beginning of NMEA sentence

GPGGA        		Message Header

HHMMSS.sss   			UTC of position fix

HH    	: hours    (00 .. 24)

MM    	: minutes  (00 .. 59)

SS.sss	: seconds  (00.000 .. 59.999)

DDMM.mmmm,d  			Latitude - N/S

DD    		: degrees  (00..90)

MM.mmmm	: minutes  (00.0000 .. 59.9999)

d     		: direction, N - north, S-south

DDDMM.mmmm,d 			Longitude - E/W

DDD		:degrees  (00..180)

MM.mmmm	:minutes  (00.0000 .. 59.9999)

d 			:direction, E - east, W-west

q            			GPS Quality indicator

q  : 0 - Fix not available, or invalid

1 - GPS SPS Mode, fix valid

2 - Differential, GPS SPS Mode, fix valid

3 - GPS PPS Mode, fix valid

ss           			Number of satellites in use (in tracking)

ss    : 0 .. 12

h.h          			Horizontal dilution of precision

h.h   : HDOP

a.a          			Antenna altitude re: mean-sea-level (geoid)

M            			Units of antenna altitude, meters

NULL         		Geoidal separation (Not supported)

NULL         		Units of geoidal separation (Not yet supported)

x.x          			Age of Differential GPS data(NULL)

xxxx 			Differential reference station ID

*CC<CR><LF>	Check Sum and sentence termination delimiter

Example.

$GPGGA,084131.430,2505.9144,N,12145.0509,E,1,05,2.0,59.1,M,,,,0000*38

**Checksum Field: The absolute value calculated by exclusive-OR the 8 data

bits of each character in the Sentence,between, but excluding

“$” and “*”. The hexadecimal value of the most significant

and least significant 4 bits of the result are convertted to two

ASCII characters (0-9,A-F) for transmission. The most

significant character is transmitted first.

2.RMC-Recommended minimum specific GPS/Transit data

and fix related data for a GPS receiver.

The format is as following:

$GPRMC,HHMMSS.sss,a,DDMM.mmmm,d,DDMM.mmmm,d,z.z,y.y,ddmmyy,d.d,v

*hh<CR><LF>

$            				Beginning of NMEA sentence

GPRMC        			Message Header

HHMMSS.sss   			UTC of position fix

HH    : hours    (00.24)

MM    : minutes  (00..59)

SS.sss: seconds  (00.000 .. 59.999)

a            	 			status (A=valid, V=invalid)

invalid if over current DOP mask

DDMM.mmmm,d  		Latitude - N/S

DD    : degrees  (00..90)

MM.mmmm: minutes  (00.0000 .. 59.9999)

d     : direction, N - north, S-south

DDDMM.mmmm,d  		Longitude - E/W

DDD   : degrees  (00..180)

MM.mmmm: minutes  (00.0000 .. 59.9999)

d     : direction, E - east, W-west

z.z          				speed over ground(knots)

0 if over current DOP mask

y.y          				Course over ground(reference to true north)

0 if over current DOP mask

ddmmyy       			UTC date of position fix

dd    : day   (1...31)

mm    : month (01..12)

yy    : year  (00..99)

d.d          				(Null)Magnetic variation(degrees) (0.0 .. 180.0)

v            				(Null)Variation sense (E=east,W=west)

*hh<CR><LF>	 		Check Sum and sentence termination delimiter

Example:

$GPRMC,084119.430,A,2505.9101,N,12145.1214,E,19.80,265.26,260799,,*39

3.The GSA - GPS DOP and Active Satellites

GPS receiver operating mode, satellites used in the navigation

solution reported by the $--GGA sentence, and DOP values.

$GPGSA,a,x,s1,s2,s3,s4,s5,s6,s7,s8,s9,sA,sB,sC,p.p,h.h,v.v*hh<CR><LF>

GPGSA        			GSA message header

a,           			Mode:

A - Automatic

M - Manual(forced to operate in 2D or 3D mode

x,           			Mode: 	1 = Fix not available

2 = 2D

3 = 3D

s1,...,sC    			1-12 PRN number of satellites used in solution

(NULL for unused fields)

p.p,         			PDOP

h.h          			HDOP

v.v          			VDOP

*hh<CR><LF>	 	Check Sum and sentence termination delimiter

Example:

$GPGSA,A,3,09,17,08,26,23,29,,,,,,,2.5,1.7,1.8*33

4. The GSV - GPS Satellites in view

Number of satellites in view, PRN numbers, elevation, azimuth,

and SNR value.  Four satellites max. per transmission, additional

satellite data sent in second or third message. Total number of messages

being transmitted and the number of the message being transmitted is

indicated in the first two fields.

$GPGSV,<a>,<m>,<nn>,

<ss>,<ee>,<aaa>,<cc>,

<ss>,<ee>,<aaa>,<cc>,

<ss>,<ee>,<aaa>,<cc>,

<ss>,<ee>,<aaa>,<cc>*hh<CR><LF>

<a>            	Total number of messages   (1 .. 3)

<m>            	Message number          (1 .. 3)

<nn>           	Total number of satellites in view

for each visible satellite (four groups per message)

<ss>           	Satellite PRN number       (1 .. 32)

<ee>           	Elevation, degrees          (00 .. 90)

<aaa>          	Azimuth, degrees True      (000 .. 359)

<cc>           	SNR (C/No)              (00 .. 99)

Null when not tracking

*hh<CR><LF>	 Check Sum and sentence termination delimiter

Ex.

$GPGSV,2,1,06,09,70,054,45,17,64,249,43,08,59,203,46,26,27,048,39*7E

$GPGSV,2,2,06,23,46,336,43,29,12,270,39*7A

5.The GLL - Geographic Position-Latidude/Longitude

The format is as following:

$GPGLL,DDMM.mmmm,d,DDDMM.mmmm,d,HHMMSS.ss,a*CC<CR><LF>

$            			Beginning of NMEA sentence

GPGLL        		Message Header

DDMM.mmm,d  		Latitude - N(+)/S(-)

DD     : degrees  (00..90)

MM.mmmm: minutes  (00.000 .. 59.9999)

d      : direction, N - north, S-south

DDDMM.mmmm,d 	Longitude - E(+)/W(-)

DDD    : degrees  (00..180)

MM.mmmm: minutes  (00.000 .. 59.9999)

d      : direction, E - east, W-west

HHMMSS.ss    		UTC of position fix

HH     : hours	 (00...24)

MM     : minutes  (00..59)

SS.ss  : seconds  (00.00..59.99)

a            			status 	: A - valid

: V - invalid

*CC<CR><LF>	 	Check Sum and sentence termination delimiter

6.The VTG - Course Over Ground and Ground Speed

The actual course and speed relative to the ground.

$GPVTG,t.t,T,m.m,M,s.s,N,g.g,K*hh<CR><LF>

t.t       			Course Over Ground (degrees True)

0 if over current DOP mask

T         		Units: T - degrees True

m.m       		Course Over Ground (degrees Magnetic)

0 if over current DOP mask

M         		Units: M - degrees Magnetic

s.s       		Speed (knots)

0 if over current DOP mask

N         		Units: N - knots

g.g       		Speed (Km/hr)

0 if over current DOP mask

K         		Units: K - Km/hr

*hh<CR><LF>	 Check Sum and sentence termination delimiter